## Slide 1
Assignment # 3
Ayman, Robert
Delay and Buffering in Wireless Networks

## Slide 2: Topology
2 nodes, 1 access point
Nodes 1 and 2 send to 0, each 10 meters apart from receiver

## Slide 3: Setup details
Simulation time: 150 sec
dataRate_ fixed at 11 Mb/Sec (IEEE 802.11b)
2 TCP connections using FTP applications
Packet Size
  Deterministic: 1500 bytes
  Random: 500 - 5000 bytes
Queueing Strategies
  Drop Tail
  Priority Queues
Buffer Size ranges from 3 to 20

## Slide 4: Throughput
Notes: Random is higher as expected
The buffer increases almost linearly, peaks around 17 packets

## Slide 5: Delay
Notes: Random is higher as expected due to bigger packets
Increases linearly, it hits a plateau around 16
16 has higher delay than 20, due to retransmissions and waiting times

## Slide 6: Drop Ratio
Notes: We can see that priority queue has consistently fewer drops especially with lower buffer sizes
Packet size doesn’t affect the drop ratio as expected, the queueing strategy does

## Slide 7: Optimal Buffer Size
Depends on Evaluation metric
  Want to maximize Throughput?: 18 buffer size (gain 20kBps throughput, gain 3ms delay)
  Want to minimize Delay?: 3 buffer size (lose 50kBps throughput, lose 12ms delay)
Middle Ground
  10 ~ 14
  Having Buffer size ranging between 10 and 14 strikes a good balance between Throughput and Delay
Changing the buffer size from 20 to 10 loses only 20kBps, but loses 3ms in delay
Notes: As the buffer size decreases, throughput and delay also decreases almost linearly

## Slide 8: Q & A